## Slide 1
Wireless Local Area Network
Submitted By:
Tanvir Islam
ID: IT-21027
Session: 2020–2021
4th year,2nd semester
Submitted To:
Dr. Md. Nazrul Islam
Associate Professor
Dept of ICT, MBSTU

## Slide 2
1. Introduction
What is WLAN?
A Local Area Network without physical cables. Uses radio waves to transmit data. Covers a limited area — home, office, or campus. Devices can move freely while staying connected.

## Slide 3
2. Historical Background
1970s
First experiments with wireless networking
2000s
WLAN became popular in homes & offices
1997
IEEE introduced 802.11 standard
2020+
Wi-Fi 6 and 6E offer multi-gigabit speeds
1999
Wi-Fi Alliance formed to certify devices

## Slide 4
3. Working Principle of WLAN
1
Devices send and receive data via Access Point (AP)
3
Router connects WLAN to the Internet
2
Communication happens over radio frequencies (2.4 or 5 GHz)
Diagram: Router in center → devices connected wirelessly
4
Data packets are transmitted using protocols

## Slide 5
4. Architecture of WLAN
Basic Service Set (BSS)
One AP and clients
Distribution System (DS)
Connects multiple BSS together
Extended Service Set (ESS)
Multiple APs connected
Stations (STA)
All wireless devices

## Slide 6
5. Components of WLAN
Access Point (AP) – creates wireless signal
Router – provides network connectivity
1
3
Antenna – transmits and receives signals
5
Wireless Adapter – built into devices
SSID – network name
2
4

## Slide 7
6. Types of WLAN Operation Modes
Infrastructure Mode
Devices connect via AP
Ad-hoc Mode
Devices connect directly (peer-to-peer)
Hybrid Mode
Combination of both

## Slide 8
Standard | Frequency | Max Speed | Introduced | Common Name
802.11a | 5 GHz | 54 Mbps | 1999 | Wi-Fi 1
802.11b | 2.4 GHz | 11 Mbps | 1999 | Wi-Fi 2
802.11g | 2.4 GHz | 54 Mbps | 2003 | Wi-Fi 3
802.11n | Dual Band | 600 Mbps | 2009 | Wi-Fi 4
802.11ac | 5 GHz | 1 Gbps | 2013 | Wi-Fi 5
802.11ax | Dual Band | 10 Gbps | 2019 | Wi-Fi 6
7. IEEE 802.11 Standards

## Slide 9
8. Advantages of WLAN
No physical cables
Easy to install & expand
Portable and flexible
Supports mobility
Multiple devices at once

## Slide 10
9. Disadvantages & Security Issues
1
Limited range
3
Signal interference (microwave, Bluetooth)
2
4
Slower than wired LAN
Security risks — hacking, data theft

## Slide 11
Disadvantages of WLAN
Extra Part: WLAN Security Methods
WEP, WPA, WPA2, WPA3 encryption
Firewalls and MAC address filtering

## Slide 12
10. Applications of WLAN
1
3
Hospitals & Airports
5
IoT & Industrial Automation
2
Campus Networks
4
Business Organizations
Home Wi-Fi & Smart Homes

## Slide 13
11. Future Developments in WLAN
Wi-Fi 7 (802.11be) – ultra-high speed
Improved AI-based signal optimization
Integration with 5G networks
Energy-efficient WLAN systems
IoT connectivity for billions of devices

## Slide 14
12. Conclusion
WLAN revolutionized local networking
1
Balances mobility, cost, and performance
3
Enables seamless, wireless communication
Plays a key role in smart technology
2
4

## Slide 15
Thank You